SECTION 10235

FLOOD VENTS

** NOTE TO SPECIFIER ** Smart Vent Products, Inc.; Foundation flood venting system products.
.
This section is based on the products of Smart Vent Products, Inc., which is located at:
430 Andbro Dr. Unit 1
Pitman, NJ 08071
Tel: 877-441-8368
Email: info@smartvent.com
Web: www.smartvent.com
Smart Vent Products, Inc. is the worldwide leading manufacturer of foundation flood venting systems and takes pride in having the a FEMA-Accepted and ICC-ES Certified flood vent product line. Founded in 2001, products are made in the United States out of marine grade 316 stainless steel. Smart Vent Products offers both wet and dry floodproofing products with solutions for any application, whether it is residential or commercial.
Smart Vent Products has a complimentary Plans Review Division where a team of Certified Floodplain Managers and Engineers will customize a floodproofing layout on your plans, run a Flood Zone Determination, check compliance and potential flood insurance rates, and more. Get started today by sending your Flood Zone plans to plans@smartvent.com.

- GENERAL

SECTION INCLUDES

** NOTE TO SPECIFIER ** Delete items below not required for project.

Flood vents.

RELATED SECTIONS

** NOTE TO SPECIFIER ** Delete any sections below not relevant to this project; add others as required.

Section 03300 - Cast in place concrete: Concrete Forming and Accessories.

Section 04090 - Masonry Accessories: Cavity Drainage, Weepholes, and Vents.

Section 04400 - Stone Assemblies.

Section 04800 - Masonry Assemblies.

Section 06100 - Rough Carpentry: Wood Frames and Framing.

Section 07900 - Joint Sealers.

Section 08360 - Overhead Doors.

Section 10700 - Exterior Specialties.

REFERENCES

** NOTE TO SPECIFIER ** Delete references from the list below that are not actually required by the text of the edited section.

ASCE/SEI 24-98, Flood Resistant Design and Construction.

ASCE/SEI 24-05, Flood Resistant Design and Construction.

ASCE/SEI 24-14, Flood Resistant Design and Construction.

FEMA, 44-CFR, Part 59-60 and 60.3 National Flood Insurance Program (NFIP).

FEMA/FIA-TB 1-2008, Openings in Foundation Walls and Walls of Enclosures for Buildings Located in Special Flood Hazard Areas.

NER-624, National Evaluation Report No. NER-624. July 2007.

International Code Council ICC-ES Acceptance Criteria for Automatic Foundation Flood Vents (AC-364). October 2007

International Code Council ICC-ES Acceptance Criteria for Mechanically Operated Flood Vents (AC-364). October 2013.

Federal Emergency Management Association's MEMO W-08086, October 2008

UL - Test for Fire Dampers in conjunction with flood vents.

DESIGN / PERFORMANCE REQUIREMENTS

SMART VENT Products Flood Vents are Engineered Openings comply with the following:

Certifications:

International Code Council - Evaluation Service Report (ESR-2074) including Florida Building Code Supplement, California Building and Residential Code Supplement.

Florida Building Product Approval (FL5822) approved for use in High Velocity Hurricane Zones (HVHZ).

Compliance:

ICC-ES Acceptance Criteria for Mechanically Operated Flood Vents (AC364).

FEMA Technical Bulletin 1: Openings in Foundation Walls and Walls of Enclosures (TB-1).

NFIP Bulletin W-08086.

NFIP Flood Insurance Manual.

American Society of Civil Engineers: Flood Resistant Design and Construction (ASCE 24-14).

International Residential Codes (IRC)

International Building Codes (IBC)

Florida Building Code (FBC)

California Building and Residential Code (CBC and CRC).

SUBMITTALS

Submit under provisions of Section 01300.

Product Data: Manufacturer's data sheets on each product to be used, including:

Preparation instructions and recommendations.

Storage and handling requirements and recommendations.

Installation methods.

Manufacturer's Certificates: Certify products meet or exceed specified requirements.

QUALITY ASSURANCE

Manufacturer Qualifications: Company specializing in manufacturing products specified in this section with minimum 5 years documented experience.

Installer Qualifications: Installer with experience on projects of a similar size and scope with similar installation conditions.

DELIVERY, STORAGE, AND HANDLING

Deliver and store materials to site in manufacturer's original, unopened containers and packaging, with labels clearly identifying product name and manufacturer.

Store products in clean, dry area indoors until ready for installation. Store materials in accordance with manufacturer's instructions.

Protect materials and finish from damage during handling and installation.

SEQUENCING

Ensure that locating templates and other information required for installation of products of this section are furnished to affected trades in time to prevent interruption of construction progress.

Ensure that products of this section are supplied to affected trades in time to prevent interruption of construction progress.

WARRANTY

Provide the manufacturer's limited 15 year warranty.

- PRODUCTS

MANUFACTURERS

Acceptable Manufacturer: Smart Vent Products, Inc., which is located at: 430 Andbro Dr. Unit 1; Pitman, NJ 08071; Tel: 877-441-8368; Email:request info (info@smartvent.com); Web:www.smartvent.com

** NOTE TO SPECIFIER ** Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

Substitutions: Not permitted.

Requests for substitutions will be considered in accordance with provisions of Section 01600.

** NOTE TO SPECIFIER ** Edit the following paragraphs as required and applicable to project requirements. Select the type and the model required and delete those not required..

FLOOD VENTS

General: Vents are constructed of Marine Grade 316 Stainless Steel formed and smooth-welded with a rigid construction. Frames are designed for installation in masonry, concrete, or framed walls, stud walls, garage doors and metal panels. Vents have a pivoting door assembly that is fitted with two patented sealed floats that provide vermin protection and immediately and automatically release the door upon contact with rising water to relieve unbalanced lateral forces on foundation walls. All flood vents are required to work bi-directionally, without human intervention.

Dual Function Flood Vent Series: Provide both flood protection and natural air ventilation. Louvered blades are temperature controlled with a bimetal coil and the screen is vermin resistant:

SMART VENT Products Model # 1540-510: Ventilated with Louvered Blades and Screen.

Flood Coverage: 200 sq.ft.

Air Ventilation: 51 sq.in.

Size: 16 inches W by 8 inches H.

Rough Opening: 16-1/4 inches W by 8-1/4 inches H.

SMART VENT Products Model # 1540-511 Double or Stacking Model: Ventilated with Louvered Blades and Screen.

Flood Coverage: 400 sq.ft.

Air Ventilation: 102 sq.in.

Size: 16 inches W by 16 inches H.

Rough Opening: 16-1/4 inches W by 16-3/8 inches H.

SMART VENT Products Model # 1540-150202 (1540-0039) 2 x 2 Multi-frame: Ventilated with Louvered Blades and Screen.

Flood Coverage: 800 sq.ft.

Air Ventilation: 204 sq.in.

Size: 32-1/2 inches W by 16 inches H.

Rough Opening: 33 inches W by 16-3/8 inches H.

SMART VENT Products One Piece Multi-Frame Model:

Amount of vents wide: ______ (No more than six)

Amount of vents high: _______(No more than three)

Flood Coverage: _____ sq.ft. (Amount of vents multiplied by 200)

Air Ventilation: _______ sq.in. (Amount of vents multiplied by 51)

Insulated Series: Provide flood protection only. Styrofoam insulation with perimeter weatherstripping.

FLOOD VENT Products Model # 1540-520: Flush or Solid Insulated Door.

Flood Coverage: 200 sq.ft.

Insulated core R-Value: 8.34

Size: 16 inches W by 8 inches H.

Rough Opening: 16-1/4 inches W by 8-1/4 inches H.

FLOOD VENT Products Model # 1540-521 Stacking Model: Flush or Solid Insulated Doors.

Flood Coverage: 400 sq.ft.

Insulated core R-Value: 8.34

Size: 16 inches W by 16 inches H.

Rough Opening: 16-1/4 inches W by 16-3/8 inches H.

FLOOD VENT Products Model # 1540-150202 (1540-0239) 2 x 2 Multi-frame: Flush or Solid Insulated Door.

Flood Coverage: 800 sq.ft.

Insulated core R-Value: 8.34

Size: 32-1/2 inches W by 16 inches H.

Rough Opening: 33 inches W by 16-3/8 inches H.

FLOOD VENT Products #1540-570 Wood Stud Wall Model: Flush or Solid Insulated Doors.

Flood Coverage: 200 sq.ft.

Insulated core R-Value: 8.34

Size: 14-1/2 inches W by 8-3/4 inches H.

Rough Opening: 14-1/2 inches W by 8-3/4 inches H.

FLOOD VENT Products #1540-524 Overhead Garage Door Model: Flush or Solid Insulated Doors, standard finish powder-coated white.

Flood Coverage: 200 sq.ft.

Insulated core R-Value: 8.34

Size: 16 inches W by 8 inches H.

Rough Opening: 16 inches W by 8 inches H.

FLOOD VENT Products #1540-574 Overhead Garage Door Model: Flush or Solid Insulated Doors, standard finish powder-coated white.

Flood Coverage: 200 sq.ft.

Insulated core R-Value: 8.34

Size: 14-1/2 inches W by 8-1/2 inches H.

Rough Opening: 14-1/2 inches W by 8-1/2 inches H.

FLOOD VENT Products One Piece Multi-Frame Model:

Amount of vents wide: ______ (No more than six)

Amount of vents high: _______(No more than three)

Flood Coverage: _____sq.ft. (Amount of vents multiplied by 200)

** NOTE TO SPECIFIER ** Fire dampers are used in conjunction with select vent. Select the Model required from the following paragraphs and delete those not required. Delete entirely if Fire Dampers are not required.

Fire Dampers: UL Rated.

Fire-Rated Dual Function Vent Model # 1540-530: 2 hour fire rated with fusible link damper. For use in masonry walls in conjunction with Dual Function Flood Vent Model #1540-510.

Fire-Rated Flow Thru Vent Model # 1540-530: 2 hour fire rated with fusible link damper. For use in masonry walls in conjunction with Insulated Series Vent Model #1540-520.

Fire-Rated Flow Thru Vent Model # 1540-537: 2 hour fire rated with fusible link damper. For use in wood walls in conjunction with Insulated Series Vent Model #1540-570.

** NOTE TO SPECIFIER ** Select the accessories required from the following paragraphs and delete those not required. Stainless steel straps are standard and provided with each vent.

Accessories:

Installation Clips, four for each vent, with the exception for Wood Wall, Overhead Door, and Multi-frame models.

Hurribond or equivalent adhesive for masonry or concrete surfaces.

Adjustable wrench for thru-bolted models and screwdriver for stud wall models.

Trim and Sleeves: Sleeves for use in ' un-filled' masonry and for, Fire Walls where ' air-space' is required on Exterior Walls and to finish off the inside of openings:

Adjustable Sleeve/Trim #1540-531-12: 8 inches to12 inches.

Adjustable Sleeve/Trim #1540-531-15: 12 inches to15 inches.

Wood Wall Model 1540-570 Interior Trim Flange #1540-573, 4 inch.

Wood Wall Model 1540-570 Interior Trim Flange #1540-573, 9 inch.

Vinyl Buck(s) #1540-800 Series for new poured concrete walls.

** NOTE TO SPECIFIER ** Powder coat finish is optional. Delete if not required.

Powder-Coat Finish with Color as follows:

** NOTE TO SPECIFIER ** Select color required and delete those not required, Check with Factory for availability of other colors.

Black

White

Gray

Wheat

Custom

Sealant: Provide joint sealers as specified in Section 07900. Only Fire-Rated sealant shall be used on Fire-Rated walls or openings.

- EXECUTION

EXAMINATION

Do not begin installation until substrates have been properly prepared.

Verify vent locations are ready to receive work, and dimensions are as indicated on shop drawings or as instructed by manufacturers.

If substrate preparation is the responsibility of another installer, notify Architect of unsatisfactory preparation before proceeding.

PREPARATION

Clean surfaces thoroughly prior to installation.

Review and coordinate setting drawings, templates, and related items that are to be embedded in concrete and masonry.

Verify that no obstructions exist that will interfere with the proper operation of the vents.

Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

INSTALLATION

Install in accordance with manufacturer's instructions.

Install vents in at least two different walls spaced evenly around foundation perimeter, and located a maximum of 12 inches higher than the, interior or exterior grade, to the bottom of vent.

Install vents plumb, level, square, true to line, and rigid.

Attach vents securely in place using fasteners supplied or approved by manufacturer.

Separate incompatible materials to prevent galvanic corrosion.

** NOTE TO SPECIFIER ** Select one of the following paragraph as required to suit the project conditions and delete those not applicable.

Install one single height flood vent for every 200 sq. ft. of enclosed space below floodplain.

Install one double height flood vent for every 400 sq. ft. of enclosed space below floodplain.

Install one quad assembly flood vent for every 800 sq. ft. of enclosed space below floodplain.

Install one multi-frame for every _______sq. ft. of enclosed space below the floodplain.

Adjust flood vents for proper operation.

PROTECTION

Protect installed products until completion of project.

Touch-up, repair or replace damaged products before Substantial Completion.

SCHEDULES

** NOTE TO SPECIFIER ** Retain Paragraph below if required to suit project requirements. Identify products by name on the Drawings or use this paragraph to define the location of each type of material to be used. The following are some examples of schedule references. Edit as required to suit project or delete and identify products on the Drawings.

:

:

END OF SECTION